## Slide 1
ASME TURBO EXPO 2026 · GT2026-175147
Turbo-Design: Open-Source Radial Equilibrium Turbomachinery Solver
Part I — Turbines. A Python framework for radial equilibrium analysis with extensible loss models.
Dr. Paht Juangphanich, Dr. Arman Mirhashemi (NASA Glenn) · William Andress (Purdue) · June 2026
github.com/nasa/turbo-design

## Slide 2
01 · MOTIVATION
Motivation
Legacy radial-equilibrium codes are poorly documented; commercial codes are closed-source; neither was built for machine-learning loss models.
NASA’s legacy radial-equilibrium tools — TD2, AXOD, and RTD — were written in Fortran 77 in the 1970s–90s. Their assumptions are poorly documented and difficult to extend. Commercial alternatives like AxSTREAM and AXIAL are proprietary, which makes it hard for academia and government to add custom physics or plug in machine-learning inference. Modern designs reduce losses through 3D optimization and advanced cooling, but legacy cascade-based loss models can’t capture those gains.
Open source, written in Python — easy to verify, modify, and extend
Modular loss-model interface — drop in custom correlations or trained ML inference models
Handles both axial and radial machines from a unified formulation
01 · Motivation
02

## Slide 3
02 · OVERVIEW
Outline
02 · Overview
03
03
Coordinate system and geometry
Meridional-velocity frame; smooth hub/shroud curves for accurate curvature
04
Governing equations
Radial-equilibrium derivation, retaining the meridional-curvature term
05
Solver modes
Pressure-balance and angle-matching, with the stability envelope
06
Turbine loss models
Legacy correlations as B-spline fits; ML-ready modular interface

## Slide 4
03 · GEOMETRY
Coordinate system and geometry
Velocity decomposition. The angle α is measured from V to the meridional Vₘ.
Built for radial flow paths
Angles are defined relative to the meridional velocity, not the axial.
Hub and shroud are defined as smooth curves rather than the jagged blade-row endpoints of legacy codes, giving accurate radius-of-curvature and inclination angles that drive the radial-equilibrium balance.
03 · Geometry
04

## Slide 5
04 · GOVERNING EQUATION
Radial equilibrium
Four-force balance on a fluid element. The radial pressure gradient must keep the element on its streamline.
Most 1D analyses drop the last term. For axial machines that is fine — Vᵣ is small. For radial machines, where hub and shroud radii change significantly, dropping it introduces error in turning angles and streamline positions. Turbo-Design retains the term, computed as dM = (dx, dr) along the streamline.
04 · Radial Equilibrium
05
(5)
(15)
OTAC Manual [10] and Cumpsty [11]
Full derivation in Appendix A
…
Derivation

## Slide 6
05 · SOLVER
Solver modes
Pressure Balance mode
Blade angles are known. The solver balances pressure across all blade rows simultaneously using SciPy SLSQP, expressing pressures as fractional drops bounded between 0 and 1. This forces monotonic pressure decrease and improves convergence. Use for: design point analysis and off-design analysis when geometry is fixed.
Angle Matching mode
Blade angles are unknown — the solver determines them
Target mass-flow distribution from hub to shroud sets the radial loading
Adjusting that distribution controls blade twist directly
Use for: design exploration before geometry is finalized
Stability: the kinetic-energy parameter C (Appendix A) must remain below unity. As C approaches 1 the passage chokes; the solver detects this condition and reports it rather than returning NaN.
05 · Solver Modes
06
Derivation

## Slide 7
06 · LOSS MODELS
Loss models as a modular interface
Legacy correlations
Four classical loss models are digitized from their original figures and fit as B-spline surfaces:
Ainley-Mathieson (1951)
Kacker-Okapuu (1982)
Craig-Cox (1970)
Traupel (1966)
CSV datasets are open in the repository so anyone can refit or audit them. Craig-Cox handles incidence — the others can be extended the same way.
Framework for ML-based loss
Common base class receives upstream + current row properties
Any inference model (PyTorch, ONNX, scikit-learn) plugs in by inheriting it
Designed for interpolation within the training space — extrapolation needs care
Trained models on real engine data are deferred to a follow-up paper
Legacy correlations and machine-learning models share the same base-class interface; substituting one for the other requires no changes to the solver.
06 · Loss Models
07

## Slide 8
07 · EFFICIENCY
Entropy-based efficiency for radial turbines
The standard total-to-total formula misleads on radial machines — entropy gives a frame-independent answer.
For radial turbines, absolute total-pressure ratio is dominated by centrifugal frame-change rather than aerodynamic loss, so the standard formula reports near-unity efficiency even with significant irreversibilities. Recasting through entropy generation isolates real losses:
where w = cP (T01 − T02) and entropy generation reduces to:
P0R is the relative total pressure — only irreversibilities reduce it.
(27b)
(27c)
07 · Entropy Efficiency
08

## Slide 9
08 · VALIDATION 1
EEE 2-stage high-pressure turbine
NASA / GE Energy Efficient Engine 2-stage HPT — meridional view: hub, shroud and blade rows (paper Fig. 8). Full-scale warm-air test measured 90.0 % efficiency.
Boundary conditions
Inlet: P₀ = 12.57 bar, T₀ = 1587 K, M = 0.2 Exit: Pₛ = 2.30 bar Rotors: 12400 RPM Fluid: air, variable cₚ and γ
CFD reference
ADS solver, Wilcox k–ω, y⁺ < 1, adiabatic walls, 30k iterations to convergence.
08 · Validation 1 — EEE
09
EEE Tutorial

## Slide 10
09 · EEE RESULTS
EEE — Turbo-Design vs CFD
09 · EEE Results
10
Quantity | Source | Stage 1 | Stage 2
Efficiency η | CFD | 0.962 | 0.970
 | Turbo-Design | 0.955 | 0.986
 | Error | 0.7 % | 1.65 %
Stage loading ψ | CFD | 1.61 | 1.20
 | Turbo-Design | 1.56 | 1.26
 | Error | 3.1 % | 5.0 %
Mass flow [kg/s] | CFD | 29.46 (total) | 
 | Turbo-Design | 29.4 (total) | 
 | Error | 0.2 % | 
CFD-measured total-pressure loss prescribed per blade row (Eq. 22). Stage efficiency and mass flow agree within 2%.

## Slide 11
10 · VALIDATION 2
Radial turbine — where the curvature term matters
Radial turbine generated with PyTurbo-Aero; geometry as used for the CFD validation.
Test the Vᵣ · dVₘ/dM term
This is the case where dropping the curvature term in Eq 15 would matter most.
Inlet: P0R = 50 bar, T0R = 1200 K Exit: Pstatic = 25 bar Rotor: 50000 RPM, γ = 1.35 A zero-loss stator upstream of the rotor enforces α₁ = 0; α₂ is matched to the CFD rotor-inlet angle.
10 · Validation 2 — Radial
11

## Slide 12
11 · RADIAL RESULTS
Radial turbine — Turbo-Design vs CFD
11 · Radial Results
12
Quantity | 1D model | CFD | Difference
P₀ loss (Yp) | 0.136 | 0.136 | prescribed
Total-total efficiency | 0.803 | 0.797 | +0.8 %
Total-static efficiency | 0.338 | 0.334 | +1.3 %
Total mass flow [kg/s] | 0.299 | 0.292 | +2.2 %
Enthalpy power [kW] | 23.23 | 22.45 | +3.5 %
Euler power [kW] | 23.23 | 22.46 | +3.5 %
T₀ inlet [K] | 1222.9 | 1222.9 | 0.0 %
T₀ exit mean [K] | 1152.6 | 1174.1 | −1.8 %
P₀ inlet [Pa] | 536,657 | 536,657 | 0.0 %
P₀ exit mean [Pa] | 427,458 | 428,240 | −0.2 %
β₁ avg [deg] | 0.01 | 0.12 | ~0 %
β₂ avg [deg] | 51.2 | 51.7 | −1.0 %
Single-rotor radial turbine, γ = 1.35. Pressure loss coefficient Yp = 0.136 prescribed from CFD.

## Slide 13
12 · CONCLUSIONS
Conclusions
Summary
Turbo-Design is an open-source Python radial equilibrium solver that replaces the legacy Fortran codes TD2 and AXOD2. The governing equations are derived from first principles, retaining the meridional curvature terms required for radial machines. Axial and radial turbines are handled with a unified formulation. The solver was validated against CFD for the NASA EEE two-stage HPT and an internally developed radial turbine, with agreement within 2% on mass flow and efficiency when supplied with CFD-measured loss coefficients.
Future work
Loss models tuned to specific turbomachinery stages
Machine-learning loss models trained on high-fidelity data
Compressor support, both axial and radial (Part II)
Continued validation against experimental datasets
Source code, tutorials, and CFD validation cases are available at
github.com/nasa/turbo-design
12 · Conclusions
13
github.com/nasa/turbo-design

## Slide 14
NASA GLENN · PURDUE · ASME GT2026-175147
Thank you
paht.juangphanich@nasa.gov | github.com/nasa/turbo-design
Paht’s open-source projects